## Slide 1: PlaatProtect (Burglar / Fire Alarm Centre) Open Source Project
W.B.J. van der Plaat
(Principal IT Architect)

## Slide 2: Questions
How can I protect my family and house against burglars?
How can I protect my family and house against fire?

## Slide 3: Idea
Lets create an application which detect movement & fire in my house and activate the necessary counter measure.
Web enabled
Use low cost hardware
Use Z-Wave technology
Use Zigbee technology

## Slide 4: PlaatProtect - Features
Burglar / Fire Alarm Centre on Raspberry Pi
  Integrate Webcams
    Motion detection with auto recording
  Integrate Zigbee meshwork
    Control lights
    Fire detector
  Integrate Z-Wave meshwork
    IR detector(s)
    Alarm Horn
  Notification
    Push Message to Mobile
    Email
  Scenario support
    Home, Sleep, Away

## Slide 5: PlaatProtect Software Architecture
REST
Interface
Zigbee
Interface
Z-Wave
Interface
Webcam
Interface
Database Layer
Business Logic Layer
Presentation Layer
Google Charts
Email Push Service
WS / JSON
PHP/CSS/JS
PHP
MySQL
PHP
Operating
System
Debian Linux
Vendor Support
Philips HUE
Vendor support
Google Protect
Vendor support
Sony
Logitec
Vendor support
- Aeotec
- Aeon
Apache
Mobile Push Service

## Slide 6: Used hardware
Raspberry Pi 3B
Philips Hue Light Bulb
Philips Hue Light Strip
Z-Wave USB Dongle
Z-Wave Aeon Horn
Z-Wave Aeotec IR detectors
Google Nest Protect
USB Webcam

## Slide 7
Raspberry Pi
PlaatProtect
Sense Hat (Pi)
Wifi Router
Webcam
1
ADSL Router
Internet
USB
USB
Z Wave
(mesh network)
Ethernet
Webcam
2
IR
Detector
Alarm
Horn
Wifi
Notification
USB
Ethernet
Ethernet
Zigbee
(mesh network)
Light
Bulb
Light
Strip
Hardware View – Configuration 1
IR
Detector

## Slide 8
Raspberry Pi
PlaatEnergy
PlaatProtect
Sense Hat (Pi)
Solar
Converter
Digital Energy
Meter
Digital Gas
Meter
Wifi Router
P1 cable
Webcam
1
Wifi
Bluetooth
ADSL Router
Internet
USB
USB
Z Wave
(mesh network)
Ethernet
Webcam
2
Wifi
USB
Ethernet
Ethernet
Zigbee
(mesh network)
Light Bulb
Light
Strip
USB
Hardware View – Configuration 2
Notification
Z Wave
(mesh network)
IR
Detector
Alarm
Horn
Fire
Detector

## Slide 9: Scenario – Home
Garage
IR
Detector
PlaatProtect
Garage
Light
Bulb
Movement
Alarm
Activate
Bulb
Log Event
In Database

## Slide 10: Scenario – Sleep
PlaatProtect
Bulb Lights
Movement
Or
Vibration
Alarm
Activate
Base
Ground
Light Bulbs
Garage
IR
Detector
Kitchen
IR
Detector
Hall
IR
Detector
Living Room
IR
Detector
Webcam
Front door
Webcam
Garden
Movement
Detected
Horn
Activate
Horn
Cloub Storage
Video
Stream
Event
Data

## Slide 11: Scenario – Away
Garage
IR
Detector
PlaatProtect
Activate
all
Light Bulbs
in House
Kitchen
IR
Detector
Hall
IR
Detector
Living Room
IR
Detector
Send
push message
to mobile(s)
Send
Email
Activate
Horn
Webcam
Front door
Webcam
Garden
Bulb Lights
Mobile
Horn
Email
Movement
Or
Vibration
Alarm
Activate Drone
“Search and …..”
PiZorg
Movement
Detected
TOP
SECRET
Video
Stream
Cloub Storage
Event
Data

## Slide 17
IR
Detector
More info
visit
plaatsoft.nl